## Slide 1: Fast Fourier Transform
FFT
The Butterfly Algorithm
Algorithm design and analysis
Seyed Mahdi Mahdavi Mortazavi
Seyed Mohsen Razavi Zadegan Jahromi
IN THE NAME OF ALLAH

## Slide 2: Contents
Part 1 – Signal analysis
Discrete signals
Fourier Transform (FT)
Discrete Fourier Transform (DFT)
Applications of Fourier Transform (Frequency modulation (FM) and noise reduction (filtering))

## Slide 3: Contents
Part 2 – Algorithm analysis
Disadvantages of DFT
Fast Fourier Transform (FFT)
Butterfly Algorithm (a solution for FFT method)
Code review
Review some examples
FFT applications and advantages

## Slide 4: Part 1 – Signal analysis
Joseph Fourier
1768 – 1830

## Slide 5: Discrete signal
Actually, a discrete signal is only limited in time (as independent variable), but not limited in value (as dependent variable).
A discrete signal is a signal (function) that does not have a continuous behavior for all values on the time axis. Actually, the discrete signal is only limited in time (as independent variable), but not limited in value (as dependent variable). A special form of this signal is the digital signal that we deal with in computers.

## Slide 6: Fourier Transform (FT)
At first, let’s check the concept of Fourier Transform:
Fourier transform is usually used to convert a signal in the time spectrum to a signal in the frequency spectrum. Examples of waves in the time spectrum are audio signals, electrical signals, and mechanical vibrations. The Fourier transform actually uses the principle that any nonlinear function can be represented by an infinite sum of sine waves. The image below shows the concept of displaying a signal with the sum of sinusoidal signals.
The Fourier transform decomposes a time-domain signal and provides information about the frequencies of all the sine waves needed to construct the time-domain signal.

## Slide 7: Fourier Transform (other examples)

## Slide 8: Discrete Fourier Transform (DFT)
An important concept: Differences between Discrete-time Fourier Transform (DTFT) and Discrete Fourier Transform (DFT):
The Discrete-time Fourier Transform (DTFT) is the (conventional) Fourier transform of a discrete-time signal. Its output is continuous in frequency and periodic; For example: to find the spectrum of the sampled version of a continuous-time signal or of a discrete-time signal of .
The Discrete Fourier Transform (DFT) can be seen as the sampled version (in frequency-domain) of the DTFT output. It's used to calculate the frequency spectrum of a discrete-time signal with a computer, because computers can only handle a finite number of values. It is periodic as well and can therefore be continued infinitely.
Method | Input | Output
DTFT | Discrete, Infinite | Continuous, Periodic
DFT | Discrete, Finite | Discrete, Finite

## Slide 9: DFT vs DTFT (Formula)
DTFT (and IDTFT) Formula
DFT (and IDFT) Formula
Differences between the formula of DTFT and DFT (mathematical review):

## Slide 10: Applications of Fourier Transform
Perhaps the most important reason for using the Fourier transform is to reduce the Noise. In signal processing, Noise is a general term for unwanted (in general, unknown) modifications that a signal may suffer during capture, storage, transmission, processing, or conversion. Two of the best ways to remove signal noise (denoising) are Modulation and Filtering. Modulation is the encoding of information of a signal in a carrier wave by varying (usually increasing) one of the characteristics of our signal wave; Wave characteristics: Amplitude, Frequency, Wavelength, Time Period and Speed; Speed of a ways = Frequency Wavelength . One of the best modulations is Frequency Modulation (FM); As you know, most music is played through FM (Frequency Modulation) radio in which we call FM wave.

## Slide 11: Advantages of Frequency Modulation (FM)
What is the advantage of Frequency Modulation?
Frequency modulation (FM) is the encoding of information in a carrier wave by varying (usually increasing) the frequency of the wave. In radio transmission, frequency modulation has a good advantage over other modulation; Actually, Frequency Modulation decreases the noise; hence, there is a significant increase in the signal-to-noise ratio (SNR)*; Meaning it will reject radio frequency interferences much better than other modulations. It also reduces the interference by the adjacent channels through guard bands.
Due to this major reasons, most music is played through FM (Frequency Modulation) radio (compared to other modulations: Amplitude modulation (AM) and Phase modulation (PM)).

## Slide 12: Two Types of Modulation
Amplitude Modulation (AM)
Frequency Modulation (FM)

## Slide 13: Noise Filtering
Review of different noise reduction (filtering) methods; Low, Band and High pass filters. In signal processing, noise reduction can be achieved in both the time domain as well as frequency domain; In case of the latter, Fourier Transform or Wavelet Transform of the observed signal is obtained and subsequently an appropriate filter is applied. A way to denoising a signal is removing the noised points in frequency domain; How? With using low, band and high pass filters with an index frequency and reject lower or higher frequencies than index frequency (or reject signals between two index frequencies).
Charts are in the frequency domain (continuous); is the Angular frequency.
Where is Period;
And is frequency.

## Slide 14: Review some real examples #1
A picture with its Fourier transform (using DFT) signal (Amplitude and Phase)

## Slide 15: Review some real examples #2
A picture in different states (Clean, Noisy, Denoised) #1

## Slide 16: Review some real examples #3
A picture in different states (Clean, Noisy, Denoised) #2

## Slide 17: Part 2 – Algorithm analysis
The Butterfly Algorithm

## Slide 18: Disadvantages of DFT
Discrete Fourier transform (DFT) implementation requires high computational resources and time; A computational complexity of order for a signal of size N. This time complexity is very high for a large number of points.
Let's review the Discrete Fourier Transform (DFT) formula. As you can see, it has very high time complexity (for many points) and complex calculations.

## Slide 19: Complexity of DFT
These transformations (with DFT and IDFT) are quite time-consuming and to understand this, we will describe DFT formula in more detail:

## Slide 20: Fast Fourier Transform (FFT)
Often in Digital Signal Processing applications it is necessary to estimate the signal spectrum, or vice versa, knowing the signal spectrum calculate the signal itself. For this purpose digital technology uses the Discrete Fourier Transform (DFT) and Inverse Discrete Fourier Transform (IDFT), which are described by formulas of DFT and IDFT.
Fast Fourier Transform (FFT) is an algorithm that computes the discrete Fourier transform (DFT) of a sequence, or its inverse (IDFT). An FFT rapidly computes such transformations by factorizing the DFT matrix into a product of sparse (mostly zero) factors. As a result, it manages to reduce the complexity of computing the DFT from which arises if one simply applies the definition of DFT, to , where is the data size. The difference in speed can be enormous, especially for long data sets where may be in the thousands or millions. many FFT algorithms are much more accurate than evaluating the DFT definition directly or indirectly. There are many different FFT algorithms based on a wide range of published theories; Here we review one of them that named Butterfly Algorithm (using Divide & Conquer).

## Slide 21: Butterfly algorithm
In the context of fast Fourier transform algorithms, a butterfly is a portion of the computation that combines the results of smaller discrete Fourier transforms (DFTs) into a larger DFT, or vice versa (breaking a larger DFT up into subtransforms). The name "butterfly" comes from the shape of the data-flow diagram in the radix-2 case, as described in the first slide of Part 2. The earliest occurrence in print of the term is thought to be in a 1969 MIT technical report.
James William Cooley
1926 – 2016
Most commonly, the term "butterfly" appears in the context of the Cooley–Tukey FFT algorithm, which recursively breaks down a DFT of composite size into smaller transforms of size where is the "radix" of the transform. These smaller DFTs are then combined via and butterflies. The Cooley-Tukey algorithm is named after James William Cooley and John Wilder Tukey.
John Wilder Tukey 1915 – 2000

## Slide 22: Review an example
Consider this example:
We have 8 points ; So the DFT formula becomes like this:
Lets separate Even points and Odd points:

## Slide 23: Review an example
Simplification for Even points:
Simplification for Odd points:

## Slide 24: Review an example
Combining the Even and Odd points:
and are periodic with period ; So lets calculate and . To do this we should calculate :

## Slide 25: Example to Proof
So we will have:
Finally we can using this conjunction, to decrease the complexity of the DFT. Generally we have this (if we have points):
Note: must be a power of 2; Why? Refer to Slide 21;

## Slide 26: Butterfly algorithm diagram
Suppose that , then we have this diagram for :
Did you see the Butterfly?!

## Slide 27: Butterfly algorithm diagram

## Slide 28: Code review #1
DFT

## Slide 29
FFT

## Slide 30: Code review #2
FFT

## Slide 31: Review some examples
Size of input |  |  |  | 
DFT runtime |  |  |  | 
FFT runtime |  |  |  | 
numpy.fft() runtime |  |  |  | 
Size of input |  |  |  | 
DFT runtime |  |  |  | 
FFT runtime |  |  |  | 
numpy.fft() runtime |  |  |  | 
Runtime of different test cases in seconds.
For each test case, answers are similar up to 10 decimal places.

## Slide 32: Thank You.
FFT
The Butterfly Algorithm
Seyed Mahdi Mahdavi Mortazavi
Seyed Mohsen Razavi Zadegan Jahromi
Github repo: